“The first to attract our attention is PLYNLIMMON (795856) to which a long and rough cart track ascends from Eisteddfa Gurig. Within the shadow of the highest mountain in Mid-Wales, its situation at 1800 ft above sea level is bleak in the extreme, with shocking weather for much of the year. Even so, drought often brought the water-powered machinery to a stand, so that one way or another the elements played havoc with operations both above ground and below. Under such conditions a considerable output of lead ore (3270 tons) was nevertheless achieved.

The mine commenced production in 1866, after a working miner found solid galena about 3 inches wide in the stream. Results were immediate and highly promising; the adit penetrated 155 fathoms in good ore and when a new company took possession in 1870, about 1000 tons had already been sold, with one foot of galena still showing in the 12 fathom level. A new 50 ft diameter water wheel started work on 26th October 1870 and the old 40 ft wheel thenceforth served for crushing and drawing. But water supplies proved so unreliable that within a year an 18 inch horizontal steam engine costing £700 was installed and connected by gearing to the pumping wheel.

Captain John Garland succeeded John Paul as manager in February 1873 - a position which the latter was no doubt glad enough to relinquish. In addition to the shortage of power, great difficulty persisted in attracting labour to so desolate a spot, where the lack of a nearby public house presented ' a grievous fault in the eyes of the miners '.

At the 1875 A.G.M. it was admitted that the steam engine had proved totally useless, having almost shaken the pumping wheel to pieces, and in the October a breakage occurred in the line of flat rods to the new shaft (sunk on rising ground to the east). Hardly was this repaired when the balance bob broke in two. However these setbacks were minor compared to lack of water for pumping, and for long periods flooding rendered the bottoms unworkable.

Although £38,000 of ore had been raised by the end of 1876, Plynlimmon still failed to pay costs and a new concern took over in the following year. Previously the winzes below the 24 fathom level were drained by the primitive expedient of man power, which was soon replaced by a system of wire ropes from the 50 ft wheel to pumps via the adit. Further troubles included the bursting of the reservoir in December 1876. But by now, lead prices were on the verge of decline, and twelve years of struggle ended in 1878 when the 36 fathom level turned out poorer than expected,

In spite of the record, Plynlimmon revived a few years later and yielded 195 tons of ore between 1887 and 1891. Apart from a little further work in 1895 it has lain dormant ever since.

Today the dumps (still with good specimens of galena) point like some giant finger down the valley, with the shafts, tramroads and wheelpits forming their own memorial to one of the most discouraging mine sites in Wales.